## Slide 1
Binary Neural Net Design Contest
Background Information
Greg Stitt
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Introduction
We will be creating an FPGA accelerator for binary neural nets (BNNs)
  Specifically, a fully connected BNN for classification
  Design should ideally work for any topology, but will be evaluated for specific topology for digit recognition
    Classifies input images into 0-9 categories
You are provided with:
  Testbench + reference model (behavioral, not synthesizable)
  DUT interface + configuration parameters
  See https://github.com/greg-stitt-uf/bnn_fcc_contest
You will:
  Implement the DUT so that the testbench passes
  Optimize the DUT for a specific use case

## Slide 3: Use Cases
Two use cases:
  Minimize latency
  Maximize throughput
Constraints
  Resources
    Both use cases will have some resource constraints, will likely require a specific FPGA
  Clock
    You might be required to achieve some minimum clock frequency (will be announced later)
Maximum throughput limited by bandwidth of input bus
  It takes minimum of 98 cycles to load a new image
    If you generate faster than that, you can increase input bus width (64 by default)
    Or, you can also optimize for latency after achieving this maximum throughput for the 64-bit bus
    Or, you can focus on maximizing clock frequency for the 64-bit bus
If you want to target a different use case, you can ask for permission

## Slide 4: Background
Multi-layer perceptron (MLP)
  Form of artificial neuron net (ANN)
Consists of:
  Input layer (some number of inputs)
  One or more “hidden” layers
    All inputs provided by previous layer to each neuron in current layer (i.e., fully connected)
    Each neuron generates an output that is fed to the next layer
  Output layer
    Similar to hidden layers but modified to generate application-specific output
    Binary classification: 1 bit
    Multi-class classification: clog2(# of classes) bits
    Regression: bits depend on precision of output, usually a real value

## Slide 5: Background: Neurons
Input (x) and weight (w) pairs are multiplied and added together with a bias (b)
Activation function provides neuron output (y)
x1
x0
x3
x2
w1
w0
w3
w2
+
+
+
Activation
*
x0
w0
*
x1
w1
*
x2
w2
*
x3
w3
y
+
b
y
b

## Slide 6: Background: MLP Topology
MLP “topology” defined by number of inputs, number of layers, and number of neurons in each layer
  Sometimes input layer isn’t shown or included in number of layers
  We will use the following notation: 2 → 4 → 2
Hidden Layer:
Input Layer:
Output Layer:
No computation
Each neuron performs 2 multiplies and 2 adds
Layer performs 8 multiplies and 8 adds
Each neuron performs 4 multiplies and 4 adds
Layer performs 8 multiplies and 8 adds

## Slide 7: Project Topology
We’ll be using the “SFC” (small, fully connected) topology from the FINN paper:
  Umuroglu, Y., Fraser, N. J., Gambardella, G., Blott, M., Leong, P., Jahre, M., & Vissers, K. (2017). FINN: A Framework for Fast, Scalable Binarized Neural Network Inference. In Proceedings of the 2017 ACM/SIGDA International Symposium on Field-Programmable Gate Arrays (pp. 65-74). DOI: 10.1145/3020078.3021744
Application is 0-9 digit recognition
  We’ll train a model for the SFC topology using the MNIST dataset
  https://www.tensorflow.org/datasets/catalog/mnist
  Classifies images as digits 0-9
Topology is 784 → 256 → 256 → 10
  Input is 28x28 8-bit pixel image: 784 total inputs
  Two hidden layers, each with 256 neurons
  Output layer has 10 neurons (one output for each possible digit)

## Slide 8: Why BNNs?
Let’s initially assume this 784 → 256 → 256 → 10 topology uses the neurons shown earlier
  Each neuron in the first hidden layer performs 784 multiplications
  Each neuron in the second hidden layer and output layer performs 256 multiplications
  Total multiplications = 784*256 + 256*256 + 256*10 = 268,800 multiplications
MLPs are computationally expensive!
  And this is for a small topology
Optimization strategy: quantization
  Reduce precision of computation (e.g., 32-bit float to 16-bit fixed)
  This makes each multiplication cheaper, but still expensive

## Slide 9: Why BNNs?
What if we reduce the precision down to one bit?
  Every weight and input is a single bit
  Aka: a “binary” neural net
The entire mult → add → activation can be replaced with:
  xnor → “popcount” → threshold comparison
  Multipliers replaced with cheap xnor
  Add tree replaced with population count
    Population count just counts asserted bits from xnor
    Often called “count ones” or “Hamming weight”
  Activation replaced with: popcount >= threshold
Not mathematically equivalent and requires special training, but
  Can sometimes achieves comparable accuracy at much lower hardware costs

## Slide 10: MLP Neuron vs BNN Neuron
xi xnor wi is same as xi == wi
Popcount counts # of matches between inputs and weights
Neuron “fires” (outputs 1) if the # of matches reach threshold
+
+
+
Activation
*
x0
w0
*
x1
w1
*
x2
w2
*
x3
w3
y
+
b
xnor
popcount
>=
x0..3
w0..3
threshold
y

## Slide 11: Neuron Processor (NP) Architecture
xnor
popcount
x[0..Pw-1]
threshold
y
NP accepts Pw weights/inputs per cycle
  Pw: parallel weights/inputs
  If neuron’s inputs/weights N <= Pw, NP requires only one pass
  For N > Pw, accumulate the popcounts of each iteration
  Total number of iterations = ceil(N / Pw)
    N = 128, PW = 16, each NP requires 8 iterations to complete a neuron
Important: pipelining options and valid logic not shown
Basic building block of entire BNN
  BNN simply replicates NP and steers data to each instance
  Data movement is significant challenge
Significant optimization potential for different use cases
  Can be easily pipelined
  Can specialize popcount and xnor for different Pw
w[0..Pw-1]
+
>=

## Slide 12: Neuron Processor (NP) Architecture
xnor
popcount
x[0..Pw-1]
threshold
y
What happens if N is not a multiple of Pw?
  NP has to receive multiples of Pw
Cheapest option: round up and pad
  e.g., N = 12, Pw = 8, round N up to 16 with 4 padded weights
  Pad extra weights and inputs in a way that doesn’t affect output
  For non-binary neural nets, padding weights with 0 would work because of multiplication by 0
    But, BNN doesn’t perform multiplication
  Remember what the binary neuron is doing:
    Counting matches between weights and inputs
  If we pad the weights to ensure differences with the input, it will not affect the popcount
    E.g. use 1s to pad weights, use 0s to pad inputs
Other options: masking
  Add masks that causes popcount to ignore padded bits
    Much more expensive
w[0..Pw-1]
+
>=

## Slide 13: Translating Problem to BNN
Input is 8-bit pixels, must be “binarized” for BNN
  We’ll use a simple threshold:
    If pixel >= 128 then input is 1 else 0
Output layer needs special treatment
  If binarized, the BNN would simply output 10 bits (one for each digit)
  Problem: unless only one output is asserted (unlikely), no way to identify most probable digit
  Solution: Output layer skips the thresholding comparison, outputs popcount value
    Additional logic (argmax) chooses output based on neuron with maximum popcount
    i.e. output layer outputs counts, argmax returns the output with the largest count

## Slide 14: Translating Problem to BNN
Binarize Inputs
argmax
Layer 1 (hidden): 256 784-input neurons
Layer 2 (hidden): 256 256-input neurons
Layer 3 (output): 10 256-input neurons (outputs popcount)
Layer 0 (input): 784 1-bit inputs (no neurons)
Input: 28x28 8-bit pixels
…………
…………
…………
…………
Output: 4-bit classification (0-9)

## Slide 15: DUT (bnn_fcc) Interface
DUT: bnn_fcc (binary neural net, fully connected classifier)
Three main ports, all AXI4 streaming interfaces
Configuration port:
  Streams weights & thresholds for every neuron in every layer
  Bus width is configurable, but set to 64 in the testbench
  Config stream provided before any image inputs
  Later slide shows stream’s data format
Input port:
  Streams 8-bit pixels over configurable-width bus (defaults to 64 bits)
  Stream starts after configuration complete
Output port:
  DUT provides stream of 8-bit classification outputs
  Actual 4-bit outputs must be expanded to 8 bits due to AXI byte requirement
bnn_fcc
config
data_in
data_out
clk
rst
64
64
8

## Slide 16: Configuration Format
The config port streams in all weights and thresholds
  Messages are specific to a layer
    Config stream provides two messages per layer (one for weights, one for thresholds)
  Provided in format that imitates network communication
Configuration header (1st 128-bits of message stream)
Bit Field | Name | Width | Description
[7:0] | msg_type | 8 | 0 = Weights, 1 = Thresholds.
[15:8] | layer_id | 8 | Index of the current layer.
[31:16] | layer_inputs | 16 | Exact fan-in (e.g., 784) of layer_id (ignore when msg_type=1)
[47:32] | num_neurons | 16 | Total number of neurons in layer_id.
[63:48] | bytes_per_neuron | 16 | Number of bytes in the payload per neuron.
[95:64] | total_bytes | 32 | Total payload bytes for the message.
[127:96] | reserved | 32 | Reserved for future use.

## Slide 17: Configuration Format
Payload immediately follows configuration header
  Length in bytes specified by total_bytes field in header
For weights (msg_type=0), payload packs weights for each neuron in the layer in consecutive order
  Neuron weights are byte-aligned to simplify parsing
  Requires padding if neuron weights aren’t a multiple of 8
  Unused bits padded with 1s to avoid affecting popcount
Simple example (10 weights per neuron):
  Neuron 0: weights b0101101110
  Neuron 1: weights b0010001010
01101110 // Byte 0: Neuron 0, weights 0-7
11111101 // Byte 1: Neuron 0, 6 padded bits + weights 8-9
10001010 // Byte 2: Neuron 1, Weights 0-7
11111100 // Byte 3: Neuron 1, 6 padded bits + weights 8-9

## Slide 18: Configuration Format
For thresholds (msg_type=1), payload packs 32-bit thresholds for each neuron in the layer in consecutive order
Simple example:
  Neuron 0: threshold = 32
  Neuron 1: threshold = 7
00100000 // Byte 0: Neuron 0 threshold byte 0
00000000 // Byte 1: Neuron 0 threshold byte 1
00000000 // Byte 2: Neuron 0 threshold byte 2
00000000 // Byte 3: Neuron 0 threshold byte 3
00000111 // Byte 4: Neuron 1 threshold byte 0
00000000 // Byte 5: Neuron 1 threshold byte 1
00000000 // Byte 6: Neuron 1 threshold byte 2
00000000 // Byte 7: Neuron 1 threshold byte 3

## Slide 19: Memory Architecture and Data Layout
Where to store data after parsing it?
  You will need to design your own custom memory architecture
    And, figure out how to organize the data across the architecture (data layout)
  Examples
    Put all weights in one large block RAM addressable by layer, neuron, and input
      Conceptually simple, but restricts parallelism
    Separate block RAM for each neuron processor
      Store the weights for all neurons that will be executed on that processor across all layers
    Separate block RAM for each neuron processor in each layer
    Separate block RAMs for weights and thresholds
      Probably a good idea to simplify addressing logic
“Configuration Manager” will parse data from stream and store it in appropriate on-chip memory
  Most important part of the entire project
  All other parts rely on memory architecture

## Slide 20: Overall Architecture
Completely up to you, but I suggest something like this:
Configuration
Manager
Weight/Threshold Memory Architecture
Neuron Processors
I/O Buffers
argmax
Input Binarization
Configuration Stream
Input/Image Stream
Output Stream
Parses config stream and writes weights/thresholds to on-chip memory
On-chip memories that provide stream of weights and thresholds to each processor
Buffer I/O for each layer
Parallel neurons (possibly across layers or all within a single layer)
Selects the highest popcount neuron from the output layer

## Slide 21: Overall Architecture
Neuron Processor 0
Threshold RAM
Weight RAM
I/O Buffer
I/O Buffer
Neuron Processor 1
PN to PW Conversion
. . . . . . . . . . . . . .
Each processor has its own separate weight and threshold RAM
PW
Threshold RAM
Weight RAM
PW
PW
Neuron Processor PN-1
Inputs fan-out to all neuron processors
Outputs are stored PW bits at a time to align with the next layer
PW
NPs generate PN bits at a time, but I/O buffers must provide PW bits at a time

## Slide 22: Overall Architecture
In general, number of neurons in a layer will exceed PN
  Processors will be shared across multiple actual neurons
  e.g., 16 total neurons in layer, 2 neuron processors
  Processor 0 handles neurons 0, 2, 4, 6, 8, etc.
  Processor 1 handles neurons 1, 3, 5, 7, 9, etc.
Configuration manager must take this into consideration when storing weights/thresholds
Neuron Processor 0
Threshold RAM
Weight RAM
I/O Buffer
Neuron Processor 1
PW
Threshold RAM
Weight RAM
PW

## Slide 23: Parallelization Strategies
One layer at a time
  Prioritizes latency of each individual layer at cost of throughput
Multiple layers at a time
  Each layer takes longer, but better throughput
All layers in parallel
  Each layer is slow, but throughput likely best
  Throughput limited to latency of slowest layer, which might suffer from fewer allocated resources
Use same PN and PW for all layers?
  Greatly simplifies configuration manager
  But, restricts parallelism
    E.g., might want a higher PW for first hidden layer, which has many inputs (784 vs. 256)
Recommendation: start simple, maybe even PN=1, PW=1
  Get it working, then increase parallelism and parameterize
  Or, set PN=PW=8 to initially eliminate all width conversion challenges
    Explained in future presentation